## Slide 1: Homework
DrĂgan andrei

## Slide 2: Exercise 7. Simplify the following Boolean functions of 4 variables given by their values 1, using Quine’s method.
f8(1,1,1,1) = f8(1,1,1,0) = f8(1,1,0,0) = f8(1,0,0,0) = f8(0,0,0,0) = f8(0,0,1,0) = f8(1,0,1,1) = f8(0,0,1,1) = 1
PROBLEM STATEMENT.

## Slide 3: General - DEFINITIONS.
Informally, to simplify a Boolean function given in a disjunctive canonical form, means to cover all its minterms with a minimum number of maximal monoms and with a minimum number of overlaps.
The simplification process is formalized by the steps below.
The initial function f is transformed into DCF(f).
Factorization process => the set of maximal monoms => M(f).
From the set of maximal monoms the central monoms are selected => C(f).
The case of the simplification algorithm is identified and all simplified forms are obtained.

## Slide 4: Quine’s Method
This method can be used for Boolean functions of any number of variables. It is also an analitical method.
STEPS:
The Boolean function f, is given in DCF => we compute Sf = {(x1,…,xn)|f(x1,…,xn) = 1}
We order Sf in ascending / descending order, with respect to the number of “1” values in each n-uple.
The minterms from the function's expression are represented using the powers of variables, in a tableau, each minterm on a line, in ascending/descending order, with respect to the number of “1” values in the n-uples of the support of the function. The header of the tableau contains the variables' names.

## Slide 5: Quine’s Method
STEPS:
4. We make groups of minterms (delimited by horizontal lines), such that all the minterms belonging to the same group have the same number of values 1 as powers of variables. A double horizontal line marks the end of the representation of the initial function.
5. Only two neighbor groups can contain two adjacent (neighbor) monoms.
6. The result of the factorization of two neighbor monoms (m and m') is a new monom represented as a row at the end of the tableau. The row contains the same values (0,1, or -)in the columns corresponding to the common variables (of m and m') and the symbol “-” for the variable which is eliminated. The rows corresponding to m and m' are marked (on the left side), with the meaning that they are not maximal monoms.
7. All the monoms obtained as results of the factorization of two neighbor groups will form a new group (delimited by a horizontal line), used further in higher order factorizations.

## Slide 6: Quine’s Method
STEPS:
8. The symbol “-” cannot be combined with anything else. Thus, beginning with double factorization only rows from two neighbor groups having “-” on the same position can be combined.
9. A double horizontal line symbolizes the end of a simple, double, triple,... factorization. The end of the factorization process is represented by a triple horizontal line.
10. The set of maximal monoms contains the monoms corresponding to all the unmarked rows from the tableau.
11. For obtaining the central monoms it is used a new tableau representing the correspondence between the maximal monoms (on columns) and the minterms from the function's expression (on rows).

## Slide 7: Quine’s Method
STEPS:
12. A cell in the tableau is marked with a star (*) if the minterm corresponding to the row was used in factorization to obtain the maximal monom from the column. A maximal monom is a central monom if there is a * (on its column), which is unique on its row. The disjunction of all central monoms belongs to all simplified forms of the initial function.
13. According to the previous tableau, the minterms from the function's expression which are uncovered by the central monoms will be covered in all possible ways using a minimum number of unused maximal monoms, with a minimum number of overlaps, resulting all simplified forms of the initial function.

## Slide 8
f8(1,1,1,1) = f8(1,1,1,0) = f8(1,1,0,0) = f8(1,0,0,0) = f8(0,0,0,0) = f8(0,0,1,0) = f8(1,0,1,1) = f8(0,0,1,1) = 1
Sf = { (0,0,0,0), (1,0,0,0), (0,0,1,0), (1,1,0,0), (0,0,1,1), (1,1,1,0), (1,0,1,1), (1,1,1,1) }
So, M(f) = {max1, max2, max3, max4, max5, max6, max7, max8 }
x1 | x2 | x3 | x4
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 0 | 1 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
Group
I
II
III
IV
V
m0
m8
m2
m12
m3
m14
m11
m15
Representation
x1 | x2 | x3 | x4
- | 0 | 0 | 0
0 | 0 | - | 0
1 | - | 0 | 0
0 | 0 | 1 | -
1 | 1 | - | 0
- | 0 | 1 | 1
1 | 1 | 1 | -
1 | - | 1 | 1
Group
VI = I + II
VII = II + III
VIII = III + IV
IX = IV + V
m0 v m8 = max1 = x̄2x̄3x̄4
m0 v m2 = max2 = x̄1x̄2x̄4
m8 v m12 = max3 = x1x̄3x̄4
m2 v m3 = max4 = x̄1x̄2x3
m12 v m14 = max5 = x1x2x̄4
m3 v m11 = max6 = x̄2x3x4
m14 v m15 = max7 = x1x2x3
m11 v m15 = max8 = x1x3x4
Simple factorization

## Slide 9
Since for each maximal monom, there is not a * (on its column), to be unique on its row => C(f) = Ø
f8S(x1,x2,x3,x4) = max1 v max4 v max5 v max8 = x̄2x̄3x̄4 v x̄1x̄2x3 v x1x2x̄4 v x1x3x4
f8S(x1,x2,x3,x4) = max2 v max3 v max6 v max7 = x̄1x̄2x̄4 v x1x̄3x̄4 v x̄2x3x4 v x1x2x3
Max monoms minterms | max1 | max2 | max3 | max4 | max5 | max6 | max7 | max8
m0 | * | * |  |  |  |  |  | 
m8 | * |  | * |  |  |  |  | 
m2 |  | * |  | * |  |  |  | 
m12 |  |  | * |  | * |  |  | 
m3 |  |  |  | * |  | * |  | 
m14 |  |  |  |  | * |  | * | 
m11 |  |  |  |  |  | * |  | *
m15 |  |  |  |  |  |  | * | *